## Slide 1: Smart Bracelets
IoT Final Challenge
Politecnico di Milano

## Slide 2: Context
Goal:
  Design, Implement, Test SW Prototype for smart bracelet
  Bracelet worn by parent and child, tracks child‘s position and triggers alarm when child goes too far

## Slide 3: Pairing Phase
Startup:
  both bracelets send a random 20-character key to uniquely couple the two devices
chi
par
Random key pre-stored
Random key pre-stored
Send key
Check if key received equals key pre-stored
If yes,
- store address of source device in memory
- send message (in unicast) to source device and stop pairing
Notes: Does is matter which of the devices sends the request? Or do both send at the same time?

## Slide 4: Operation Mode
chi
par
Listen for messages from child
Periodically transmit info messages (every 10 sec.) containing
X,Y coordinates
Estimated kinematic status (stand, walk, run, fall)

## Slide 5: Alert Mode
chi
par
Send info message
Listen for info messages from child
Receive info message
Read content
  If status = Falling:
    Send alarm
    Send X,Y coordinates of chi
- If not received message 1 min after last receive:
- send alarm “Missing“
- sent last coordinates received

## Slide 6: Implementation
Write application in OS of choice
X,Y coordinates are random numbers
Kinematic status random select from
  P(walking) = P(standing) = P(running) = 0.3
  P(falling) = 0.1
Simultaneous simulation with 2 couples of bracelets (= 4 nodes)
End simulation by moving node out of range (mote.turnOff() in .py)
Attach simulation to Tossim-live or Node-red
  Transmit alarm messages to serial port
  Display output in terminal